## Slide 1
Ethanol Content Measurement in Micro-brewed beer
Bsc. Gil Goldman
Unrestricted

## Slide 2: Thousands of liters of beer go wasted every day

## Slide 3
Gas Chromatography
NIRS and MIRS
Densitometry
Refractometry
Hydrometry

## Slide 4: How it works
Retrieve a sample
Drop hydrometer
Check Hydrometer Depth
Compare result to tables and formulas
Throw away beer sample (!)

## Slide 5
Hydrometers are everywhere
Easy to use
Simple to understand

## Slide 6
Accurate
  ±2 mm
  ±0.002 SG
  ±0.26 ABV
Low Cost
  Priority
  Less than 15 $US
Parameters

## Slide 7: Physical Architecture
Raspberry Pi Zero W
HC-SR04
DHT11
Hydrometer + Lattice

## Slide 8: Software Architecture
Python, C
Over 1000 lines of code
Modular
Maintainable, usable, extendable

## Slide 11
Final cost < 15$ USD
Distance accuracy < 1 mm
Corrected gravity accuracy < 0.002
Conclusion

## Slide 12
Happy to answer any questions
Title by Patrick Fore on Unsplash
Bottles by Adam Wilson on Unsplash
Brewery by Jeff Frank on Unsplash
Hydrometer by David Blaikie
Closing Beer by Lukas from Pexels

## Slide 13
Krausen
Low density foam
Amount depends on beer being brewed
Wider point
Small actuator

## Slide 14
Ultrasonic sensor dependence on temperature and humidity
  Humidity - Negligible
    “The variation of the specific heat ratio and the speed of sound in air with temperature, pressure, humidity, and CO_2 concentration”, O. Cramer, National Metrology Program, 1992
  Temperature – negligible within working range
    5-8 C difference due to fermentation
    “Brewing Science and Practice”, D. E. Briggs ; C. A. Boulton ; P. A. Brooks ; R. Stevens, 2004
  Pressure – Noticeable effect in high pressures
    Device working assumption is that it will not be used in extremely high or low pressures
    Mostly around 1 Atmosphere

## Slide 15
HC-sr04 Drift
  Negligible to non-existent
    “Motion Measurement Using Inertial Sensors, Ultrasonic Sensors, and Magnetometers With Extended Kalman Filter for Data Fusion”, H. Zhao; Z. Wang, IEEE sensors Journal, 2012
    Used to verify other sensors
DHT11 Temperature Drift
  Negligible
    Internal calibration routine
    “Temperature and humidity module DHT11 Product Manual”, Aosong(Guangzhou) Electronics Co.,Ltd
DHT11 Humidity Drift
  Noticeable – correction required
    Drift irrelevant, humidity function not used